## Slide 1
Clarifying the definition of Lubrication and Servicing
(MPIG 2023-03)
Wang Yi Ping
MSG-X Group, Customer Service Center, COMAC
May 13-18, 2024
IMRBPB Annual Meeting

## Slide 2
Clarifying the definition of Lubrication and Servicing
Issue: The current definition of Lubrication and Servicing in MSG-3 document is either incomplete or ambiguous, thus needs clarification.
Lubrication and Servicing | Any act of lubricating or servicing for the purpose of maintaining inherent design capabilities.
Problem:
Task Type | Interval | Task Description
SVC | 400FH | IDG oil system servicing (replenish as required)
SVC | 700FH | CHECK OIL LEVEL OF VARIABLE FREQUENCY GENERATOR (VFG) AND ADD OIL AS REQUIRED
VCK | 700FC | VISUAL CHECK OF SHIMMY DAMPER OIL GAUGE
VCK | 14DY | VISUAL CHECK OF PASSENGER/CREW ENTRY DOORS EMERGENCY OPERATION CYLINDER GAS PRESSURE GAUGE TO VERIFY IT IS IN NORMAL RANGE
Task Type | Interval | Task Description
SVC | 6000FC | Replace nose landing gear oil
SVC | 4000FC | SERVICING OF MAIN LANDING GEAR SHOCK STRUT(REPLACE HYDRAULIC OIL)
DIS | 800FH | Replace the oil in IDG oil system
DIS | 1500FH | DISCARD VARIABLE FREQUENCY GENERATOR (VFG) LUBRICATION OIL
Discussion Process: Submitted on 2023-02-02, First Presented on 2023-06-07
Agreed and Finalized on 2023 MPIG F-F meeting
Main Comments Contributors: Armando , Ravi, Alan, Leonard, RMPIG

## Slide 3
Clarifying the definition of Lubrication and Servicing
Recommendation:
Glossary
Lubrication and Servicing | Any act of lubricating or servicing for the purpose of maintaining inherent design capabilities. Lubrication is applying a lubricant directly to an item to prevent or reduce friction/corrosion/wear/fretting between moving surfaces.
Servicing | Servicing is work such as draining/replenishing/replacing of consumables (air, fuel, oil, water, etc.) to meet operating conditions or quantity requirements.
NOTE: | Tasks that determine the need for replenishment of the consumable prior to the actual act of replenishment should not be directly defined as SVC. Instead, task types, such as VCK, that can determine the need for replenishment should be considered first.
NOTE: | According to the definition of DIS, replacing the consumables (such as lubricating oil, hydraulic oil) are recommended not to select DIS task type, but SVC.
Applicability Criteria Section of SVC/LUB and DIS
CIP with Comments
CIP 2023-03

## Slide 4
Thank You
Any questions, please ping wangyiping@comac.cc