## Slide 1: Structure inspections – Self adhesive decals
Prepared by:
Francesca Tanzi
Senior Expert – Aircraft Maintenance Program (AMP)
EASA Aircraft Maintenance & CAMO Section (FS.1.2)
Date: 17/05/2024

## Slide 2: Structure inspections – Self adhesive decals
Issue
Increasing intent, and use, of paint patches, decals (also sometimes called stickers), vinyl wraps (also sometimes called “foils”) for:
  repair (typically cosmetic)
  decorative

## Slide 3: Structure inspections – Self adhesive decals
Main Risk
The use of self adhesive decals, vinyl wraps etc., as an alternative to painting, may challenge the effective accomplishment of both visual and eddy current inspections and other regulatory requirements.
  Weight & balance
  damage tolerance (damage initiation and damage modes)
  lightning performance
  material compatibility
  potential partial separation (flutter)
  part departing aircraft debris threats (system ingestion, jamming)
  maintaining access (do not cover access panels!)
  colour/temperature issues
  potential to damage baseline structure upon application and removal

## Slide 4: Structure inspections – Self adhesive decals
Where we are
Authorities:
  Some authorities request operators and maintenance organizations to address the impact on structural inspection tasks when using such decals and ensure that the aircraft maintenance programme requires their removal at the appropriate time.
Manufacturers:
  Some manufacturers are requiring the removal of decals prior to the inspections in the MRBR/MPD and AMM. However, there is no guidance, nor standards to be referred to.

## Slide 5: Structure inspections – Self adhesive decals
Where to go
How to address the potential impact on effectiveness of the maintenance inspections?
  More extensive TCH/SCH guidance in manuals (e.g. AMM, SRM)?
  Considerations to be done as part of the MRB process?
  Standards Development Body standards? (SAE Commercial Aircraft Composite Repair Committee (CACRC)?)

## Slide 6: Structure inspections – Self adhesive decals
EASA Proposal
As an interim solution, EASA proposes a standard statement to be included in the MRBR:
  "Operators and maintenance organisations are reminded that the use of paint patches, self adhesive decals, vinyl wraps (for cosmetic repairs, decoration etc) may challenge original substantiated TCH/STCH inspections (visual, NDI) and other certification requirements. Operators and maintenance organisations need to address the impact on structural inspection tasks when using paint patches, self adhesive decals, vinyl wraps and ensure that the aircraft maintenance programme requires their removal at the appropriate time.".

## Slide 7: Thank you!