## Slide 1: IMRBPB Annual Meeting (IAM) Action Item 2023-03 May 17, 2024
Presented by Jeffrey Phipps
Chief, Operational Airworthiness
Standards Branch, Transport Canada Civil Aviation (TCCA)
RDIMS #20294077
Notes: <number>

## Slide 2: Action Item (AI) 2023-03
TCCA to develop a new regulatory CIP to cover the FDR/CVR issue related to AI 2019-06 and AI 2019-07.
Intent: to amend MSG-3 to accommodate safety related system to produce tasks to maintain integrity of such systems (e.g. FDR, CVR, DLR, ULB/D, and ELT).
<number>
Notes: <number>

## Slide 3: Flight Recorder Systems
Review of:
ICAO SARPs
Industry Standards
NAA regulatory frameworks
MRBRs
<number>
Notes: <number>

## Slide 4: ICAO Annex 6 and Doc 10104
Recording Inspection:
CVR: analysis and examination of recorded data from each aircraft source and relevant external sources shall be carried out by replay to verify that all required signals meet intelligibility standards.
FDR: analysis and examination of recorded data, in engineering units, to evaluate the validity of all recorded parameters.
DLR: analysis and examination of recorded messages shall be carried out by replay.
ULB/ULD: no SARP on maintenance. DOC 10104 recommends following manufacturer’s recommendations.
<number>
Equipment | Task | Interval
CVR | Operational | Prior to first flight
 | Functional | N/A
 | Recording Inspection | 1 or 2 years (depending on system integrity)
 | Overhaul | N/A
FDR | Operational | Prior to first flight
 | Recording Inspection | 1 or 2 years (depending on system integrity)
 | Sensor inspection/calibration | ICAs or no ICAs - 2 or 5 years (depending on sensor)
 | Overhaul | N/A
DLR | Operational | Prior to first flight
 | Functional | N/A
 | Recording Inspection | 2 or 4 years (depending on system integrity)
 | Overhaul | N/A
Notes: <number>

## Slide 5: EUROCAE ED-112A and SAE 8045A
<number>
Equipment | Task | Interval
CVR | Operational | Daily
 | Functional | 6 months
 | Recording Inspection | 1 to 2 years (depending on system integrity)
 | Overhaul | N/A
FDR | Operational | Pre-flight
 | Recording Inspection | 1 or 2 years (depending on system integrity)
 | Sensor inspection/calibration | 15000 HRS/ 60 months (or by analysis of system)
 | Overhaul | Manufacturer’s recommendations (MR)
DLR | Operational | N/A
 | Functional | 24 months
 | Recording Inspection | 2 or 4 year (depending on system integrity)
 | Overhaul | MR
ULB/ULD | Operational | MR (voltage and operation)
 | Battery Replacement | MR
Notes: <number>

## Slide 6: NAA Regulatory Framework
<number>
Equipment | Task | Interval – NAA #1 | Interval – NAA #2 | Interval NAA #3
CVR | Operational | Daily | ICA | Daily or every 7 days
 | Functional | 12 months or 3000hrs | ICA | 1 or 2 years (system integrity)
 | Recording Inspection | 12 months or 3000hrs (Intelligibility) | ICA | 1 or 2 years (system integrity)
 | Overhaul | MR | N/A | 
FDR | Operational | N/A | ICA | Daily or every 7 days
 | Recording Inspection | 12 months or 3000hrs | ICA | 1 or 2 years (system integrity)
 | Sensor inspection/calibration | MR | ICA | MR or every 5 years
 | Overhaul | MR | N/A | N/A
DLR | Operational | Daily | ICA | 
 | Functional | N/A | ICA | 
 | Recording Inspection | 12 months – 3000hrs | ICA | 
 | Overhaul | N/A | N/A | 
ULB/ULD | Operational | 12 months | ICA | 
 | Battery Replacement | MR | ICA | 
Notes: <number>

## Slide 7: MRBR Tasks
<number>
Equipment | Task | MRBR #1 | MRBR #2 | MRBR #3
CVR | Operational (OPC) | 3 years | 12000 flight hours (FH) | 6000 FH or 18 months
 | Functional | N/A | N/A | N/A
 | Recording Inspection | N/A | N/A | N/A
 | Overhaul | N/A | N/A | N/A
FDR | Operational (OPC) | N/A | 12000 FH | N/A
 | Recording Inspection | 24 months | N/A | 6000 FH or 18 Months
 | Sensor inspection/calibration | N/A | N/A | N/A
 | Overhaul | N/A | N/A | N/A
DLR | Operational (OPC) | N/A | N/A | N/A
 | Functional | N/A | N/A | N/A
 | Recording Inspection | N/A | N/A | N/A
 | Overhaul | N/A | N/A | N/A
ULB/ULD | Operational (OPC) | 3 years | 12000 FH | 2 years
 | Battery replacement (DIS) | MR | MR | MR
Notes: <number>

## Slide 8: Results of Review
<number>
Notes: <number>

## Slide 9: Results of Review (cont’d)
IMPS and MSG-3
Influence of National requirements (IP 169):
  IP trying to solve the problem of some safety/emergency equipment may not have been identified as an MSI.
  IMPS (chapters 4 & 5) and MSG-3 (2-1-2.3 & 2-3-1) amended to state the development of scheduled maintenance shall not be unduly influenced by National Requirements, which was intended to mean the MSI selection process should not be influenced.
  May have helped with the identification of an MSI but may have prevented task selection?
<number>
Notes: <number>

## Slide 10: Results of Review (cont’d)
MSG-3 Analysis
Even if functional failures (evident or hidden) are identified, lack of direct adverse effect to safety:
  E.g., prevent the continued safe flight and landing.
Definition of safety/emergency systems or equipment:
  Flight data recorders do not enhance aircraft evacuation, and
  When failed, does not have an adverse effect on safety.
Does not consider other functions of recorder or equipment:
  Such as, data integrity, data preservation, use for accident/incident investigation and associated recommendations, and SAR.
Current MSG-3 task selection is not aligned with typical tasks associated with recorder system maintenance.
<number>
Notes: <number>

## Slide 11: Potential Options
NAA’s have a responsibility to establish/maintain national requirements inline with ICAO and industry standards:
  Daily, Operational Check, and Recording inspection.
  Not sure if all NAAs follow ICAO requirements or if they have filed a difference.
Amend MSG-3 to ensure systems/equipment used for accident/incident investigation and SAR purposes are analyzed:
  Impact on definitions such as safety (adverse effect), direct adverse effect on operating safety, safety/emergency systems or equipment and MSI.
  Impact on logic diagram and analysis.
Develop new analysis to address systems/equipment used for accident/incident investigation and SAR purposes, which may include flight recorders (FDR/CVR/DLR), ULD, and distress transmitters such as ELT and GADSS.
<number>
Notes: <number>

## Slide 12: Option 3 - New logic in MSG-3
New definitions required to address systems/equipment used for accident/incident investigation and search and rescue purposes.
New logic analysis to consider:
  Recording, data accuracy, integrity/preservation, location transmissions, as part of the analysis procedure (Functions, functional failures, failure effects, failure causes),
  International maintenance standards need to also be considered (type of task, intervals, how to perform).
Where would it fit into MSG-3?
  Part of current MSI selection?
  New dedicated MSI item? [e.g., MSI-AI (accident-investigation)];
  As part of 2.3 Aircraft Systems/Powerplant analysis procedure?
  New 2.7 after L/HIRF?
<number>
Notes: <number>

## Slide 13: Option 3 – Road Map
Gather examples of analysis for these systems (next 6 months),
Review examples and draft CIP (March 2025),
Send draft CIP out for review (April 2025),
Review CIP during 2025 IAM,
Revise CIP based on comments received following 2025 IAM,
Prepare and submit final version of the CIP (February 2026),
Review CIP during 2026 IAM.
<number>
Notes: <number>

## Slide 14: Questions?
<number>
Notes: <number>