## Slide 1: Interface between L/HIRF and Zonal MSG-3 analysis
L/HIRF analysis Step 11
Prepared by:
Luca Tosini
Aircraft Maintenance Expert
EASA Aircraft Maintenance & CAMO Section (FS.1.2)
Date: 17/05/2024

## Slide 2: ATA MSG-3 Rev. 2022.1 – L/HIRF Maintenance

## Slide 3: ATA MSG-3 Rev. 2022.1 – L/HIRF Maintenance
L/HIRF Protection Analysis Methodology and Logic Diagram
  Step 11: Is degradation detectible with a Zonal Inspection?
  ”The L/HIRF WG will perform an assessment using access, visibility or other means to determine if degradation is detectible by a Zonal Inspection.”
  Step 10: No dedicated L/HIRF Task
  ” NOTE: All visible components, including L/HIRF protection components, are inspected as part of the
  Zonal inspections.”

## Slide 4: ATA MSG-3 Rev. 2022.1 – L/HIRF Maintenance
L/HIRF Protection Analysis Methodology and Logic Diagram
  Step 11 implies the identification of the “degradation modes” of the L/HIRF protection.
  Step 10 represents an “exit ramp” from the MSG-3 logic, implying “No Task Selected”.
    At this point there is formally no task to transfer to the zonal program.

## Slide 5: ATA MSG-3 Rev. 2022.1 – L/HIRF Maintenance
L/HIRF Protection Analysis Methodology and Logic Diagram
  Step 10 represents an “exit ramp” from the MSG-3 logic, implying “No Task Selected”.
    At this point there is formally no task to transfer to the zonal program.
  No reference to the timely detection of the degradation of the L/HIRF protection.
    Assumption that the interval of the L/HIRF GVI, if ever identified, is ≤ than the interval of the zonal GVI.

## Slide 6: Points for Discussion
Is Step 11 properly formulated?
  Is there any need to identify the interval effective to detect the specific L/HIRF protection degradation mode?
Is Step 10 the correct analysis decision-box following a “Yes” answer to Step 11?
  Why do not apply the LHSI “zonal transfer candidate” concept as done for MSI and SSI analysis?

## Slide 7: Thank you!