## Slide 1
Use of Video Links in Procedures
March 30, 2024
Notes: 0

## Slide 2
Overview
Approximately four years ago, A4A launched an initiative to identify safety improvement opportunities related to Human Factor errors in maintenance
  The initiative intends to develop mitigations for Failure to Follow
  Specification 127 (in development)
Over the recent 18 months A4A leadership has assigned increased priority, facilitated multiple routine meetings with a leadership team of Operators, Regulators (FAA), and OEMs (airframe and propulsion).
The initiative has branched into several sub-teams:
  Simplification of Warnings, Cautions and Notes
  Simplification of how procedures are presented
    Focus on digital delivery w/nested and linked content
      More intuitive navigation
  Use of video links for point of use procedure, training and job aid
  Benchmarking

## Slide 3
Overview
The “Use of video links for point of use procedure, training and job aid” may interest IMRBPB for a couple reasons:
  Evolution to ICAs is anticipated. Initial use cases are accepted as “for reference only” under an operator's CAMP (training program).
  Advanced awareness may be helpful to harmonize forward looking NAA guidance and consider future guidance requirements
Extensive Research has been performed by FAA’s Civil Aerospace Medical Institute (CAMI) (team member)
Regulatory research has been done by Aircraft Maintenance Division Flight Standards, AFS-300 management (team member)

## Slide 4
Overview
There are many initiatives underway by highly qualified persons / teams
CAMI is one of the most longstanding
  Advocating increased applied human factor principles for the maintenance domain while reflecting the extensive successes in flight ops
The conclusion of two recent presentations are shared for your awareness:
  An FAA (Aircraft Maintenance Division AFS-300) regulatory assessment
  A Purdue presentation delivered at the December 2023 InfoShare
The full presentations are in this file
Federal Aviation
Administration

## Slide 5
Conclusions
Federal Aviation
Administration
Nothing in the paraphrased regulatory documentation (parts 43 and 121 only) provided in this presentation precludes the use of videos in maintenance instructions.
~80% of maintenance mistakes involve human error
Use of AR/VR/MR systems in parallel with procedure delivery and human decision-making may increase performance, improve safety and reduce errors.
Errors and safety concerns could be reduced w/integration of contextual information provided to AMTs

## Slide 6
Questions?
Notes: 5

## Slide 7: Overview
Provide a review of US regulations and FAA guidance pertaining to the use of video or AR utilized as maintenance instructions, or as a supplement to maintenance instructions.
ICA’s verses Air Carrier Supplementation utilizing Videos (AIR, AED, AMD)
Encourage discussion of conclusions and challenges.
We applaud this effort and say thanks for giving the FAA a seat or two at the table. (CAMI and AFS-300)

## Slide 8: 14 CFR 43.13c Performance Rules
§43.13 Performance rules (general) (Paraphrased)
(a) Each person performing maintenance, shall use the methods, prescribed in the current manufacturer’s maintenance manual or ICA, or other methods acceptable to the Administrator, except as noted in § 43.16.
NOTE: §43.16 Airworthiness limitations - Each person performing maintenance shall perform it IAW the operations specifications approved by the Administrator under part 121 or 135, or approved under § 91.409(e)
(b) Maintenance shall be at least equal to its original or properly altered
(c) Special provisions for holders of air carrier operating certificates and operating certificates issued under Pt 121, 135, or 129 operators holding operations specifications. The methods, techniques, and practices contained in the maintenance manual of an air carrier operating certificate or an operating certificate under Pt 121, 135 or 129 that is required to have a CAMP constitute acceptable means of compliance

## Slide 9: 14 CFR 121.133 Preparation
§121.133 Preparation
Each certificate holder shall prepare and keep current a manual for the use and guidance of flight, ground operations, and management personnel in conducting its operations.
(b) For the purpose of this subpart, the certificate holder may prepare that part of the manual containing maintenance information and instructions, in whole or in part, in printed form or other form acceptable to the Administrator

## Slide 10: 14 CFR 121.135 Manual Content
§121.135 Manual Contents (Paraphrased)
(a) Each manual required by § 121.133 must—
(1) Include instructions and info necessary to allow personnel to perform their duties and responsibilities with a high degree of safety;
(2) Be in a form that is easy to revise;
(3) Have the date of last revision on each page concerned; and
(4) Not be contrary to any regulations
(b) The manual must contain info appropriate for each group of personnel: Such as; maintainers, the training program, instructions for maintenance and inspections, other safety info
(c) Each certificate holder shall maintain at least one complete copy of the manual at its principal base of operations

## Slide 11: 14 CFR 121.367 Mx Programs.
§121.367 Maintenance, Preventive Maintenance, and Alterations Programs
Each certificate holder shall have an inspection program and a program covering other maintenance, preventive maintenance, and alterations that ensures that—
Maintenance, preventive maintenance, and alterations performed by it, or by other persons, are performed in accordance with the certificate holder’s manual;
(b) Competent personnel and adequate facilities and equipment are provided for the proper performance of maintenance, preventive maintenance, and alterations; and
(c) Each aircraft released to service is airworthy and has been properly maintained for operation under this part

## Slide 12: 14 CFR 121.369 Manual Requirements
§121.369 Manual requirements (Paraphrased)
(b) The certificate holder’s manual must contain the programs required by § 121.367, and must include at least the following:
(1) The method of performing routine and nonroutine maintenance
(3) The method of performing required inspections
(10) Policies, procedures, methods, instructions for the accomplishment of all maintenance. They must be acceptable to the FAA and are performed in accordance with their maintenance program and maintenance manual
(c) The certificate holder must set forth in its manual a suitable system that provides for preservation and retrieval of info in a manner acceptable to the Administrator

## Slide 13: 14 CFR 121.375 Mx Training Program
§121.375 Maintenance and preventive maintenance training program
Each certificate holder or person performing maintenance or preventive maintenance functions for it shall have a training program to ensure that each person (including inspection personnel) who determines the adequacy of work done is fully informed about procedures and techniques and new equipment in use and is competent to perform his duties

## Slide 14: Other Guidance for Consideration
AC 120-77A Performance Rules: Provisions Contained in an Operators Manual Under §43.13(c)
  This AC describes a means of compliance for commercial operators, to meet the requirements of §43.13
FAA Order 8110.54A - Instructions for Continued Airworthiness Responsibilities, Requirements, and Contents
FAA Order 8900.1 Vol 3 Chap 1 Sec 1 The General Process for Approval or Acceptance of Operator Applications
  A process of approval or acceptance of programs, procedures, to ensure items meet regulatory standards

## Slide 15: What is FAA Order 8900.1
It is a FAA order that directs the activities of Aviation Safety Inspectors (ASI)and other Flight Standards Service (FS) employees responsible for the certification, technical administration, and surveillance of air carriers, certain other air operators conducting operations in accordance with the appropriate part.
Majority of content is available to the world!
https://drs.faa.gov/browse

## Slide 16: Additional Comments / FAA Concerns
Inexperience with Video Instruction. In addition to obvious “training” for the technician, companies need a robust training program, tailored to their operations, fleet, CAMP, procedures, and generational demographic, especially if “Video’s” are to be used for additional instruction.
The overuse of warnings and caution notes becomes ineffective. OEM’s should consider prioritizing them according to risk and likelihood of non-compliance. Many manufacturers instead, use notes and warnings to limit liability, just like the FDA warnings on medications. (May require legal input)
Generational issues also need to be addressed. It is great for a new technician to have a mentor, to help them learn practical application of the training they have received, but a company needs to be deliberate in who they want mentoring their new employees. If they aren’t careful, the experienced technician will teach them “shortcuts” they have learned along the way, and then they have created baby dinosaurs. Generationally, the younger generation is typically more accustomed to learning through video’s/YouTube, and are very comfortable with utilizing AR/VR!

## Slide 17: Additional Comments Cont.
Another example is organizational culture and organizational operations pace, applying pressure on the technician to get the aircraft back in service.
Another factor to consider is environmental conditions, such as noise, working in high places, chemical fumes, poor lighting, snow, rain, wind, etc.
Fatigue. CAMI has done extensive research in this area. There are a multitude of voluntary measures that individuals and corporations may employ, to assess a person’s fatigue levels, and fitness for duty. In addition to voluntary measures, rulemaking may be necessary to move the safety needle in the area of fatigue risk management in aircraft maintenance (though unpopular with most of industry).
Checklists, if a company provides and embraces the concepts of utilizing check lists, such as in the FAA Personal Minimums checklist, it can have an impact.

## Slide 18: Further Challenges and Concerns
  Challenges may exist with acceptance until additional FAA policy and guidance is written
  Should Video’s have a caveat that mentions its purpose – (For information Only)?
  ICA’s may be a challenge, at least at first.
  Maybe start with only perfecting Supplemental Videos (Beta Test).
  Where do the Videos get placed in the instructions?
  How would Videos stand out within maintenance instructions? (For example - Click Here For a Supplemental Video)
  When is it appropriate to use Videos – Continual areas where problems arise?
  Costs, will it be labor intensive to develop?
  Revisions – who does the revisions and how often?
  Possibly require a Proof of Concept?
  Avoid stacked and or duplicated warnings and cautions (Clutter)

## Slide 19: Further Challenges and Concerns
What environment should / would they be used in? (Heavy Maintenance, Line Maintenance, Hangar Only, etc.)
Will the organizations Culture support video use.
Consistency – Should all operators and OEM’s be doing it the same way?
First - Consider the importance - Need to know vs Nice to know
Should Video’s be considered / incorporated based on a Comprehensive fix? (ASAP’s, VDRP’s, etc.)
What is EASA’s, DGAC or TC’s position?

## Slide 20: Coordination within FAA
  Safety Assurance offices (CMO’s, FSDO’s, IFO’s), along with AFS-300 (AMD), and AFS-100 (AED), will consider providing information and insight needed to develop effective guidance for inspectors, and certificate holders that want to use video technologies.
  FAA Safety Assurance offices typically will divulge any concerns and coordinate with the Aircraft Maintenance Division (AFS-300), and the Aircraft Evaluation Division (AFS-100) typically when new processes are established and initially implemented.
  AFS-300 would be the group that typically would develop any guidance, memos, info’s etc. to support video use targeted around the workgroup's efforts associated with Video's.
The Aircraft Evaluation Division (AED) assists and coordinates with aircraft manufacturers, operators, Aircraft Certification Offices, and other Flight Standards Offices with product-specific Continued Operational Safety (COS)

## Slide 21
Conclusions
Existing (FAA) Policy and Guidance
  Although additional refining more than likely would be needed, current guidance provides a performance-based framework for accepting changes to a certificate holder’s CAMP. Policy and guidance is not specific to new technologies such as the use of videos or AR in maintenance instructions.
  Nothing in the paraphrased regulatory documentation (parts 43 and 121 only) provided in this presentation precludes the use of videos in maintenance instructions.
Notes: Coordination
Existing guidance is not specific to new technologies currently (New to us all)
Important for awareness across SA, OSS, and Industry
  New technology and its use and acceptance is new to everyone
  Allows everyone to think outside the box
  Opportunities for mutual learning
Your input is important for our enhancement in guidance/more effective guidance
  More defined/effective/permanent guidance
  Open areas to other operators for 43.13(a) and (b)
  Other areas of maintenance/inspection with New technology
Coordination is not for AFS-300 or AED to concur or approve/accept the use of UAS procedures for GVI. That is part of the CMOs responsibility.
Coordination is to support with discussions on how to approach certain situations/items to consider, etc. and to allow OSS to collect information and insight needed to develop more effective guidance
Proof of Concept Idea – CMO and Certificate Holder determine a timeframe or number of inspections required to prove equivalency.
Memo is good for 2 years – expectation to either have draft guidance ready or a Notice published from the feedback provided by ACSA.

## Slide 22: The Future of Aviation Inspection: Artificial Intelligence (AI) and Mixed Reality (XR) as Agents of Transformation
Damon Lercel, MBA, PhD.
Manoj S. Patankar, MBA, PhD., FRAeS
Center for Research and Education in Advanced Transportation Ecosystems
Aviation Safety InfoShare December 2023

## Slide 23: Background
Nationally, 151,300 aviation technicians are tasked with safety work in hazardous environments that include heights, confined spaces, and extreme weather.
Importantly, the work of these technicians is aided by collaborations with highly experienced inspectors who leverage their years of prior experience as technicians to inspect, identify, and certify necessary aircraft maintenance.
Unfortunately, potential failures in these collaborations coupled with a high- stress environment and the potential to misunderstand maintenance manuals can directly lead to devastating air accidents.
Human error accounts for 70% of aviation accidents, with technical/maintenance process failure being the leading cause of airline accidents and fatalities.
Approximately 80% of maintenance mistakes involve human error.

## Slide 24: Background

## Slide 25: Introduction
Potential Impact Opportunity
  The integration of Human-AI collaboration using AI and XR in inspection may reduce human error in aviation and other industries.
  Errors and safety concerns could be remedied through the intelligent integration of contextual information that would provide AMTs with real-time data for aircraft inspections and repairs.
  Utilizing AI and XR systems in parallel with human decision-making may provide AMTs access to more instantaneous information when needed and increase overall situational awareness, thus increasing performance and reducing the number of errors.
  The incorporation of Human-AI teams via an AI and XR platform into inspection could reduce human error frequency in aviation maintenance, thereby enabling better human decision-making.

## Slide 26: Background

## Slide 29: Background

## Slide 30: Background

## Slide 31: The Research Team

## Slide 32: The Research Project

## Slide 33: The Research Project
Research Goal and Questions:
What are the potential risks and the ways to mitigate them when integrating AI and XR in aviation maintenance settings?
How can we effectively integrate AI and XR into intelligent work systems to achieve breakthroughs in aviation inspection for diverse populations?
How can we design, develop, and evaluate evidence-based interaction paradigms to combine the capabilities of humans and AI to enhance Human-AI team performance?
What are the economic and workforce impacts of integrating AI and XR technology in this domain?

## Slide 34: The Research Project
Prototype XR Simulator Currently Used by AMT Students for Training

## Slide 35: The Research Project

## Slide 36: Questions?
Dr. Damon Lercel Purdue University
Email: dlercel@purdue.edu
Dr. Manoj Patankar Purdue University
Email: mspatankar@purdue.edu

## Slide 37
Questions?
Notes: 36